## Slide 1: Parallel Iterative Solvers with the Selective Blocking Preconditioning for Simulations of Fault-Zone Contact
Kengo Nakajima
GeoFEM/RIST, Japan.
3rd ACES Workshop, May 5-10, 2002.
Maui, Hawaii, USA.

## Slide 2: I am usually working on
Solving large-scale linear equations Ax=b is the most important and expensive part of various types of scientific computing.
  for both linear and nonlinear applications
Various types of methods have been proposed and developed.
  for dense and sparse matrices
  classified into direct and iterative methods
Dense Matrices : Globally Coupled Problems
  BEM, Spectral Methods, MO/MD (gas, liquid)
Sparse Matrices : Locally Defined Problems
  FEM, FDM, DEM, MD (solid), BEM w/FMP
solving Ax=b !!!

## Slide 3: Direct Methods
Gaussian Elimination/LU Factorization.
  compute A-1 directly.

  Robust for wide range of applications.
  Good for both dense and sparse matrices

  More expensive than iterative methods (memory, CPU)
  Not suitable for parallel and vector computation due to its global operations.

## Slide 4: Iterative Methods
Stationary Methods (SOR, Gauss-Seidel etc.) and Nonstationary Methods (CG, GMRES, BiCGSTAB etc.)

  Less expensive than direct methods, especially in memory.
  Suitable for parallel and vector computing.

  Convergence strongly depends on problems, boundary conditions (condition number etc.)
  Preconditioning is required.

## Slide 5: Preconditioing for Iterative Methods
Convergence rate of iterative solvers strongly depends on the spectral properties (eigenvalue distribution) of the coefficient matrix A.
A preconditioner M transforms the linear system into one with more favorable spectral properties
  In "ill-conditioned" problems, "condition number" (ratio of max/min eigenvalue if A is symmetric) is large.
  M transforms original equation Ax=b into A'x=b' where A'=M-1A, b'=M-1b
ILU (Incomplete LU Factorization) or IC (Incomplete Cholesky Factorization) are well-known preconditioners.

## Slide 6: Strategy in GeoFEM
3D linear elastic problem for simple cubic geometry on Hitachi SR8000/MPP with 128 SMP nodes (1024 PEs) (not ES40, unfortunately).
Block ICCG Solver.
The largest problem size so far is 805,306,368 DOF.
Iterative method is the ONLY choice for large-scale parallel computing.
Problem specific preconditioning method is the most important issue although traditional ILU(0)/IC(0) cover wide range of applications.
128 SMP nodes
805,306,368 DOF
335.2 GFLOPS
16 SMP nodes
100,663,296 DOF
42.4 GFLOPS

## Slide 7: Topics in this Presentation
Contact Problems in Simulations for Earthquake Generation Cycle by GeoFEM.
  Non-linear
  Ill-conditioned problem due to penalty constraint by ALM (Augmented Lagrangean)
  Assumptions
    Infinitesimal deformation, static contact relationship.
      Location of nodes is in each "contact pair" is identical.
    No friction : Symmetric coefficient matrix
Special preconditioning : Selective Blocking.
  provides robust and smooth convergence in 3D solid mechanics simulations for geophysics with contact.
Examples on Hitachi SR2201 parallel computer with 128 processing elements.

## Slide 8
OVERVIEW
Background
General Remedy for Ill-Conditioned Problems
  Deep Fill-in
  Blocking
Special Method for Fault-Contact Problems
  Selective Blocking
  Special Repartitioning
Examples
  Large Scale Computation on Hitachi SR2201 w/128 PEs
Summary

## Slide 9
Geophysics Application w/Contact
Augmented Lagrangean Method with Penalty Constraint Condition for Contact
6,156 elements, 7,220 nodes, 21,660 DOF
840km1020km600km region

## Slide 10
● Newton Raphson iteration
▲ Solver iteration for entire
Newton Raphson iteration
■ Solver iteration for ONE
Newton Raphson iteration
Large Penalty provides
・Good N-R convergence
・Large Condition Number
Optimum Choice
Augmented Lagrangean Method
Penalty~Iteration Relation for Contact Problems
Newton-Raphson / Iterative Solver

## Slide 11: Results in the Benchmark 7,220 nodes, 21,660 DOFs, =10-8 GeoFEM's CG solver (scalar version) Single PE case
Block-type Preconditioning seems to work well for ill-conditioned cases
=1010
IC(0) : 89 iters, 8.9 sec.
DIAG : 340 iters, 19.1 sec.
Block LU scaling : 165 iters, 11.9 sec.
=1016
IC(0) : >10,000 iters, >1,300.0 sec.
DIAG : No Convergence
Block LU scaling : 3,727 iters, 268.9 sec.

## Slide 12
Background
General Remedy for Ill-Conditioned Problems
  Deep Fill-in
  Blocking
Special Method for Fault-Contact Problems
  Selective Blocking
  Special Repartitioning
Examples
  Large Scale Computation on Hitachi SR2201 w/128 PEs
Summary

## Slide 13: Ill-Conditioned Problems
The world where direct solvers have governed.
But iterative methods are the only choice for large-scale massively parallel computation.
We need robust preconditioning !!
Remedy : Basically Preconditioning like Direct Solver
  Deep Fill-in
  Blocking and Ordering

## Slide 14: Deep Fill-in : LU and ILU(0)/IC(0) Even if A is sparse, A-1 is not necessarily sparse due to fill-in.
Gaussian Elimination
do i= 2, n
do k= 1, i-1
aik := aik/akk
do j= k+1, n
aij := aij - aik*akj
enddo
enddo
enddo
ILU(0) : keep non-zero pattern of the original coefficient matrix
do i= 2, n
do k= 1, i-1
if ((i,k)∈ NonZero(A)) then
aik := aik/akk
endif
do j= k+1, n
if ((i,j)∈ NonZero(A)) then
aij := aij - aik*akj
endif
enddo
enddo
enddo
DEEP Fill-in

## Slide 15: Deep Fill-in : ILU(p)/IC(p)
LEVij=0 if ((i,j)∈ NonZero(A)) otherwise LEVij= p+1
do i= 2, n
do k= 1, i-1
if (LEVik≦p) then
aik := aik/akk
endif
do j= k+1, n
if (LEVij = min(LEVij,1+LEVik+ LEVkj)≦p) then
aij := aij - aik*akj
endif
enddo
enddo
enddo
DEEP Fill-in

## Slide 16: Deep Fill-in : General Issues
Close to direct solver if you have DEEPER fill-in.
requires additional memory and computation.
  x2 for ILU(0) -> ILU(1)
DEEP Fill-in

## Slide 17: Blocking : Forward/Backward Substitution for ILU/IC Process
Apply complete/full LU factorization in the certain size block for process D-1.
  Just divided by diagonal component for scalar cases.
3x3 block for 3D solid mechanics.
  tightly coupled 3-components (u-v-w) on 1-node.
M= (L+D)D-1(D+U)
Forward Substitution
(L+D)p= q : p= D-1(q-Lp)
Backward Substitution
(I+ D-1 U)pnew= pold : p= p - D-1Up
BLOCKING

## Slide 18: 33 Block ILU(0) Preconditioning Forward Substitution
do i= 1, N
SW1= WW(3*i-2,ZP)
SW2= WW(3*i-1,ZP)
SW3= WW(3*i ,ZP)
isL= INL(i-1)+1
ieL= INL(i)
do j= isL, ieL
k= IAL(j)
X1= WW(3*k-2,ZP)
X2= WW(3*k-1,ZP)
X3= WW(3*k ,ZP)
SW1= SW1 - AL(1,1,j)*X1 - AL(1,2,j)*X2 - AL(1,3,j)*X3
SW2= SW2 - AL(2,1,j)*X1 - AL(2,2,j)*X2 - AL(2,3,j)*X3
SW3= SW3 - AL(3,1,j)*X1 - AL(3,2,j)*X2 - AL(3,3,j)*X3
enddo
X1= SW1
X2= SW2
X3= SW3
X2= X2 - ALU(2,1,i)*X1
X3= X3 - ALU(3,1,i)*X1 - ALU(3,2,i)*X2
X3= ALU(3,3,i)* X3
X2= ALU(2,2,i)*( X2 - ALU(2,3,i)*X3 )
X1= ALU(1,1,i)*( X1 - ALU(1,3,i)*X3 - ALU(1,2,i)*X2)
WW(3*i-2,ZP)= X1
WW(3*i-1,ZP)= X2
WW(3*i ,ZP)= X3
enddo
Full LU Factorization
for 3x3 Block
D-1
BLOCKING

## Slide 19: Benchmark : Effect of Fill-in/Blocking 7,220 nodes, 21,660 DOFs, =10-8 CG solver, Single PE case
Iteration number and computation time dramatically decreases by fill-in and blocking.
=1016
IC(0) : >10,000 iters, >1,300.0 sec.
Block LU scaling : 3,727 iters, 268.9 sec.
Block IC(0) : 1,102 iters, 144.3 sec.
Block IC(1) : 94 iters, 21.1 sec.
Block IC(2) : 33 iters, 15.4 sec.
DEEP Fill-in
BLOCKING

## Slide 20
Background
General Remedy for Ill-Conditioned Problems
  Deep Fill-in
  Blocking
Special Method for Fault-Contact Problems
  Selective Blocking
  Special Repartitioning
Examples
  Large Scale Computation on Hitachi SR2201 w/128 PEs
Summary

## Slide 21: Selective Blocking Special Method for Contact Problem Strongly coupled nodes are put into the same diagonal block.

## Slide 22: Selective Blocking Special Method for Contact Problem Strongly coupled nodes are put into the same diagonal block.
Initial Coef. Matrix
find strongly coupled contact groups (each small square:3x3)
Reordered/Blocked Matrix
nodes/block
Each block corresponds to
a contact group

## Slide 23: Selective Blocking or Supernode Procedure : Forward Substitution in Lower Tri. Part
Block ILU/IC
Selective Blocking/
Supernode
size of each diagonal block depends on contact group size
Apply full LU factorization
for computation of D-1

## Slide 24: Benchmark : SB-BIC(0) Selective Blocking + Block IC(0) 7,220 nodes, 21,660 DOFs, =10-8 CG solver, Single PE case
=1016
IC(0) : >10,000 iters, >1,300.0 sec.
Block LU scaling : 3,727 iters, 268.9 sec.
Block IC(0) : 1,102 iters, 144.3 sec.
Block IC(1) : 94 iters, 21.1 sec.
Block IC(2) : 33 iters, 15.4 sec.
SB-Block IC(0) : 82 iters, 11.2 sec.

## Slide 25: Benchmark : Selective Blocking Selective Blocking converges even if =1020
BIC(1)
BIC(2)
SB-BIC(0)

## Slide 26: Benchmark : 4PE cases 7,220 nodes, 21,660 DOFs, =10-8 =1016 , CG solver
Single PE
Block IC(0) : 1,102 iters, 144.3 sec.
Block IC(1) : 94 iters, 21.1 sec.
Block IC(2) : 33 iters, 15.4 sec.
SB-BIC(0) : 82 iters, 11.2 sec.
4 PEs
Block IC(0) : 2,104 iters, 68.4 sec.
Block IC(1) : 1,724 iters, 85.8 sec.
Block IC(2) : 962 iters, 69.9 sec.
SB-BIC(0) : 1,740 iters, 70.0 sec.
In 4PE case, nodes in tightly connected groups are on different partition and decoupled.

## Slide 27: Summary
<number>
<footer>
Deep fill-in, blocking and selective-blocking dramatically improve the convergence rate for ill-conditioned problems such as solid mechanics with contact.
But performance is bad in parallel cases with localized preconditioning when nodes in tightly connected pairs are on different partition and decoupled.
Special repartitioning method needed !!

## Slide 28
Background
General Remedy for Ill-Conditioned Problems
  Deep Fill-in
  Blocking
Special Method for Fault-Contact Problems
  Selective Blocking
  Special Repartitioning
Examples
  Large Scale Computation on Hitachi SR2201 w/128 PEs
Summary

## Slide 29: Outline of the Repartitioning
BEFORE
repartitioning
Nodes in contact pairs are on separated partition.
AFTER repartitioning
Nodes in contact pairs are on same partition, but no load-balancing.
AFTER
load-balancing
Nodes in contact pairs are on same partition, and load-balanced.
Convergence is slow if nodes in each contact group locate on different partition.
Repartitioning so that nodes in contact pairs would be in same
partition as INTERIOR nodes will be effective.

## Slide 30: Special Repartitioning Benchmark: 4PE cases
BEFORE Repartitioning
AFTER Repartitioning

## Slide 31
Background
General Remedy for Ill-Conditioned Problems
  Deep Fill-in
  Blocking
Special Method for Fault-Contact Problems
  Selective Blocking
  Special Repartitioning
Examples
  Large Scale Computation on Hitachi SR2201 w/128 PEs
Summary

## Slide 32: Large-Scale Computation Description
<number>
<footer>
NX1
NX2
NZ1
NZ2
NZ1+NZ2
x= 0
x= NX1
x= NX1+1
x= NX1+NX2+1
z= 0
z= NZ1
z= NZ1+1
z= NZ1+NZ2+1
x
y
z

## Slide 33: Problem Setting & B.C.'s
<number>
<footer>
MPC at inter-zone boundaries
Symmetric condition at x=0 and y=0 surfaces
Dirichlet fixed condition at z=0 surface
Uniform distributed load at z= Zmax surface

## Slide 34: Sample Mesh 99 nodes, 80 elements.
<number>
<footer>
1
2
5
6
9
10
13
14
17
18
25
29
30
26
21
22
1
2
3
10
11
12
19
20
21
28
29
30
37
38
39
46
47
48
55
56
57
64
65
66
73
74
75
82
83
84
91
92
93
Contact
Groups

## Slide 35: Results on Hitachi SR2201 (128PEs) NX1=NX2=70, NY=40, NZ1=NZ2=70, Repartitioned. 2,471,439 DOF, 784,000 Elements Iterations/CPU time until convergence (=10-8)
<number>
<footer>
BIC(0)
/E
102
905 iters
194.5 sec.
104
106
> 8,300
> 1,800.0
108
1010
BIC(1)
225
92.5
297
115.2
460
165.6
BIC(2)
183
139.3
201
146.3
296
187.7
SB-BIC(0)
542
69.5
542
69.5
542
69.5
543
69.7
544
69.8

## Slide 36: Required Memory NX1=NX2=20, NY=20, NZ1=15, NZ2=16 83,649 DOF, 24,000 Elements
<number>
<footer>
BIC(0) 105 MB
BIC(1) 284 MB
BIC(2) 484 MB
SB-BIC(0) 128 MB

## Slide 37: Concluding Remarks
<number>
<footer>
Robust Preconditioning Methods for Contact Problem.
  General: Deep Fill-in, Blocking.
  Problem Specific: Selective-Blocking using Supernodes.
  Large-Scale Problems using 128 PEs of Hitachi SR2201.
Selective-Blocking (SB-BIC(0)) provides robust convergence.
  More efficient and robust than BIC(0), BIC(1) and BIC(2).
  Iteration number for convergence remains constant while  increases.

## Slide 38: Further Study
<number>
<footer>
Optimization for Earth Simulator.
Dynamic Update of Contact Information.
  Large Slip / Large Deformation.
  More flexible and robust preconditioner under development such as SPAI (Sparse Approximate Inverse).